## Slide 1
RDD 2026 ON-DEMAND PRESENTATION
Improvement in Inhalation Technique
During a Pharmacy-Led Connected
Inhaler Service Evaluation in Adults
with Asthma or COPD
Judith Borst, Marco Franza, Mauro Citterio, Cristina Cova, Luca Ponti, Martijn Grinovero
Apotheek De Vijfhoek | Amcor Plastiape | Amiko
Connected inhaler data paired with pharmacist coaching was associated with better inhalation technique over follow-up.
Keywords: connected inhaler; inhalation technique; pharmacy-led service; PIF
5
community pharmacies in the Netherlands
59
patients with first and last control visits
72.9%
patients improved inhalation technique
01
Notes: Hello, and thank you for viewing this RDD 2026 on-demand presentation.
This presentation is titled Improvement in Inhalation Technique During a Pharmacy-Led Connected Inhaler Service Evaluation in Adults with Asthma or COPD.
The work was conducted by Judith Borst, Marco Franza, Mauro Citterio, Cristina Cova, Luca Ponti, and Martijn Grinovero, with affiliations at Apotheek De Vijfhoek, Amcor Plastiape, and Amiko.
The central idea is simple: connected inhaler data, when paired with pharmacist coaching, may help make inhalation technique visible and actionable during routine care. In this service evaluation, 5 community pharmacies in the Netherlands enrolled patients using connected inhaler sensors, and 59 patients had both first and last control data available for analysis. Overall, 72.9% of analyzed patients improved their inhalation technique over follow-up.

## Slide 2
WHY IT MATTERS
Incorrect inhaler technique is a delivery problem that can be made visible.
01
Technique gap
Incorrect technique is common in asthma and COPD and can undermine effective drug delivery.
02
Objective signal
Connected inhaler sensors capture indicators of the inspiratory maneuver during routine use.
03
Targeted coaching
Pharmacists can use sensor-derived feedback to correct technique during normal care encounters.
The evaluation asked whether this service model changed inhalation quality between early and late follow-up.
RDD 2026 | Pharmacy-led connected inhaler service evaluation
02
Notes: Incorrect inhaler technique remains a major practical problem in asthma and COPD care. Even when the right medication is prescribed and the patient is using the inhaler, the dose may not be delivered effectively if the maneuver is not performed correctly.
Traditionally, technique assessment depends on observation, patient recall, or periodic instruction. Those approaches are useful, but they can miss what happens during everyday inhaler use.
Connected inhaler sensors offer a different kind of signal. They can capture objective indicators of the inspiratory maneuver during routine use, such as peak inspiratory flow, inhalation duration, and device orientation.
The service model evaluated here links that objective signal to pharmacist follow-up. The practical question was whether a pharmacy-led service using connected inhaler feedback was associated with better inhalation quality between early and late follow-up.

## Slide 3
SERVICE MODEL
The evaluation paired connected sensors with short pharmacy follow-up encounters.
Enroll
72 adults with asthma or COPD enrolled across five pharmacies
Measure
Connected sensors integrated with Respiro captured inhalation maneuvers
Coach
Pharmacists used objective feedback during onboarding and follow-up
Devices/platforms
Ellipta, Nexthaler, and RS01 sensors integrated with the Respiro digital platform
RDD 2026 | Pharmacy-led connected inhaler service evaluation
03
Notes: The evaluation followed a three-part routine-care model: enroll, measure, and coach.
First, adults with asthma or COPD who were already using inhaled therapy were enrolled across 5 community pharmacies in the Netherlands. 72 patients entered the service.
Second, connected sensors integrated with the Respiro platform captured inhalation maneuvers during everyday use. The devices represented in the evaluation included Ellipta, Nexthaler, and RS01 sensor integrations.
Third, pharmacists used the sensor-derived feedback during onboarding and follow-up encounters. The intent was not only to record inhaler use, but to identify specific technique issues and provide corrective coaching. Follow-up occurred over approximately one month in routine clinical practice.
This is important because the service is designed around normal pharmacy workflow rather than a highly controlled research visit.

## Slide 4
ANALYSIS
First and last control periods were compared using Good, Fair, and Poor classifications.
Good
no errors
Fair
>=1 non-critical error
Poor
>=1 critical error
First Control
Last Control
paired patient-level comparison
Wilcoxon signed-rank test
RDD 2026 | Pharmacy-led connected inhaler service evaluation
04
Notes: Inhalations were classified into three quality groups.
Good inhalations had no detected errors. Fair inhalations had at least one non-critical error. Poor inhalations had at least one critical error.
For each patient, the analysis compared the first control period with the last control period. Patient-level percentages of Good, Fair, and Poor inhalations were calculated overall and also for the individual parameters of peak inspiratory flow, inhalation duration, and orientation.
The paired first-to-last comparison was analyzed using the Wilcoxon signed-rank test. This matters because the analysis focuses on within-patient change over time, rather than comparing different groups of patients.

## Slide 5
ANALYZED COHORT
59 patients completed at least two pharmacy visits.
59
patients analyzed
40
patients with asthma
19
patients with COPD
82.1%
mean measured adherence
Population details
Asthma: 13 male / 27 female; mean age 53 years
COPD: 8 male / 11 female; mean age 66.7 years
The analyzed set reflects routine-care completion rather than a randomized controlled trial population.
RDD 2026 | Pharmacy-led connected inhaler service evaluation
05
Notes: 59 patients completed at least two pharmacy visits and were included in the first-to-last control analysis.
Of these, 40 patients had asthma and 19 had COPD. In the asthma group, there were 13 male and 27 female patients, with a mean age of 53.0 years. In the COPD group, there were 8 male and 11 female patients, with a mean age of 66.7 years.
Mean measured adherence across the analyzed group was 82.1%.
It is important to interpret this population correctly. This was a routine-care service evaluation, not a randomized controlled trial. The analyzed set reflects patients who completed the service follow-up, so the findings should be read as observed improvement within a pharmacy-led connected inhaler service.

## Slide 6
OVERALL RESULT
Good inhalations increased while Poor inhalations decreased.
Good
Fair
Poor
First Control
48.5%
22.4%
29.2%
Last Control
64.1%
17.8%
18.1%
+15.7 pp
Good inhalations; p < 0.001
-11.1 pp
Poor inhalations; p < 0.001
43/59
patients improved technique
RDD 2026 | Pharmacy-led connected inhaler service evaluation
06
Notes: The overall inhalation quality results moved in the desired direction.
Good inhalations increased from the first control period to the last control period. At last control, Good inhalations represented 64.1% of inhalations, which was an increase of 15.7 percentage points. This change was statistically significant, with p < 0.001.
Poor inhalations decreased. At last control, Poor inhalations represented 18.1% of inhalations, a reduction of 11.1 percentage points, with p < 0.001.
Fair inhalations also decreased, from approximately 22.4% to 17.8%, a reduction of 4.6 percentage points, with p = 0.05.
At the patient level, 43 of 59 analyzed patients improved their inhalation technique. That corresponds to 72.9% of the analyzed cohort.

## Slide 7
PARAMETER RESULT
PIF, duration, and orientation each shifted toward better technique.
PIF
Good
+10.6 pp
p = 0.002
Poor
-6.3 pp
p = 0.004
Duration
Good
+11.8 pp
p < 0.001
Poor
-11.8 pp
p < 0.001
Orientation
Good
+10.2 pp
p < 0.001
Fair
-10.2 pp
p < 0.001
Positive bars show gains in Good inhalations; lower error bars show reductions in Fair or Poor classifications.
RDD 2026 | Pharmacy-led connected inhaler service evaluation
07
Notes: The parameter-specific results show that improvement was not limited to one single aspect of the inhalation maneuver.
For peak inspiratory flow, Good classifications increased by 10.6 percentage points, with p = 0.002. Poor PIF classifications decreased by 6.3 percentage points, with p = 0.004.
For inhalation duration, Good classifications increased by 11.8 percentage points, and Poor classifications decreased by the same amount. Both changes had p < 0.001.
For orientation, Good classifications increased by 10.2 percentage points, while Fair classifications decreased by 10.2 percentage points. Both changes had p < 0.001.
Together, these results suggest a broad shift toward more stable and correct inhalation performance across flow, duration, and device handling.

## Slide 8
CONCLUSION
Connected inhaler data can support targeted pharmacy coaching in routine care.
What improved
Error-free inhalations increased and critical-error inhalations decreased between first and last control.
What it supports
Sensor-derived objective assessments can inform targeted corrective coaching during pharmacy follow-up.
How to interpret it
This was a routine-care service evaluation; results support feasibility and observed improvement, not randomized efficacy.
Thank you
Questions and discussion
RDD 2026 | Pharmacy-led connected inhaler service evaluation
08
Notes: In conclusion, inhalation technique improved between the initial and final assessment periods in this pharmacy-led connected inhaler service evaluation.
The most important finding is the combination of more error-free inhalations and fewer critical-error inhalations. The parameter-level analyses also support the same direction of change across peak inspiratory flow, inhalation duration, and orientation.
These findings support the role of connected inhaler technologies as part of pharmacy-led follow-up, especially when objective sensor-derived assessments are used to guide targeted corrective coaching.
At the same time, the interpretation should remain appropriate to the study design. This was a routine-care service evaluation, so the results support feasibility and observed improvement, not randomized efficacy.
Thank you for listening.